Annex B- Technical Specifications

RFQ REF: 2024/SOP/SCU/RFQ007

UNHCR Peshawar is looking to procure X-ray security screening machine to be installed at the UNHCR entrance.

| Item Description | Model/Specifications | Remarks |
| --- | --- | --- |
| X-RAY SECURITY SCREENING MACHINE | MODEL: XIS-5335-S Tunnel Opening: 53.3 cm x 35.8 cm (W x H) X-ray Generator: 160kV, Operating at 150kV Beam Direction: Diagonally Upward Conveyor Speed: 23 cm/s Forward or Reverse Conveyor Height: 72.9 cm from Floor Conveyor Capacity: 165 kg Evenly Distributed Load Wire Resolution: 40 AWG Typical, 38 AWG Standard Steel Penetration: 39 mm Typical, 37 mm Standard Memory: 4 GB RAM Platform: Windows® 10 OS Storage Capacity: 256 GB SSD Display Type: Single 21.5” Flat Panel Color Monitor Operating Temperature: 0°C - 40°C Power Requirements (XIS): 220VAC ±10%, 50Hz, 10 Amp Max •6 Color Imaging • High Penetration Function •Organic /Inorganic Imaging •Atomic Z- Number Measurement • Continuous Zoom •Auto Image Archiving • Network Ready •Real- Time Self Diagnostics • Baggage Counter INCLUSIVE: •Threat Image Projection (TIP) •Density Alert •Screener Assist Software •Enhanced Imaging™ (EI) •Entry Roller Extension of 0.5 meter for XIS5335-S •Exit Roller Extension of 0.5 meter for XIS5335-S Including at least one year warranty. |  |
| After Sale Service | The vender must provide installation and after sale services for a period of one year. |  |